## Slide 1: 4.1 Applied mathematical theory in engineering applications
Presenter name
Time and date
Location
Trigonometry – 3 Answers

## Slide 2
Learning outcomes
By the end of this session, the learner should be able to:
calculate the angles and lengths of the sides of a right-angled triangle
investigate examples for contextualising the application of trigonometry
solve worked examples of contextualised trigonometry.

## Slide 3
5 m
2 m
Starter activity
An apprentice engineer has been asked to manufacture a tool to use to check whether their work is at 90˚.
Calculate the length of the third side so that the apprentice engineer can order the right lengths of material.
a
a2 = 52 – 22
a2 =
a2 = 4.58m

## Slide 4
In our previous session, we calculated the angles and side lengths of right-angled triangles.
A great example for the practical use of this is in street lighting. Manufacturing Engineers who produce modules for street lighting columns need to know the 'cone' of light produced so that can calculate a safe coverage of lighting on a carriage way.
In the following slides, you will do those calculations.
Free to use under the Pixabay license

## Slide 5
4.5m
3.5m
Here we have a streetlight column that stands 4.5m above the ground. The light output itself is 25,000 candelas (cd). Calculate the amount of light at the point on the ground directly below the light and at 3.5m to one side.
E = the amount of light at the surface (lux).
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
E = I x cos ɸ
d2
E
I
d

## Slide 6
4.5m
3.5m
E = the amount of light at the surface (lux).
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
E = I
d12
When we do this calculation, we will have to calculate the length of the third side and calculate the angle, as our formula will change to:
E = I x cos ɸ
d22
E
I = 25,000cd
ɸ
d1
d2

## Slide 7
4.5m
3.5m
E = the amount of light at the surface.
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
E = I
d2
E = 25,000
4.52
E = 1234.57 lux
E
I = 25,000 cd
d1
ɸ

## Slide 8
4.5m
3.5m
E = the amount of light at the surface.
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
Tan ɸ = Opp
Adj
Tan ɸ = 3.5
4.5
Tan ɸ = 0.778 Tan-1(0.778) = 37.880
Cos ɸ = Cos (37.88) = 0.789
E
I = 25,000 cd
ɸ
d2

## Slide 9
4.5m
3.5m
E = the amount of light at the surface.
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
Cos ɸ = Adj
Hyp
Hyp = Adj
cos ɸ
Hyp = 4.5
0.789
Hyp = 5.70m
E
I = 25,000 cd
d
ɸ
37.880

## Slide 10
4.5m
3.5m
E = the amount of light at the surface.
I = the amount of light from the source.
d = the distance from the light source to a point on the surface (m).
E = I x cos ɸ
d2
E = 25,000 x 0.789
5.702
E = 607.1 lux
E
I = 25,000 cd
ɸ
5.70m
37.880

## Slide 11
6.5m
5.5m
Activity 1
A streetlight column stands 6.5m above the ground The light output itself is 25,000 candelas (cd). Calculate the amount of light at the point on the ground directly below the light and at 5.5m to one side.
E = I
d2
E = 25000
6.52
E = 591.71 lux
E = I x cos ɸ
d2
d2 = 6.52 + 5.52 = 72.5 d = = 8.51
cos ɸ = 6.5
8.51
E = 25000 x 0.763
8.512
E = 263.39 lux

## Slide 12
12m
10.95m
Plenary Activity
A lighting column stands in the middle of a motorway central reservation. The light stands at a height of 12m from the ground and has an output of 18,000 lumens (lm).
Calculate the amount of light at the point directly below and 10.95m (the width of half a motorway) to one side.
Free to use under the Pixabay license
E = I
d2
E = 18000
122
E = 125 lux
E = I x cos ɸ
d2
d2 = 122 + 10.952 = 263.903
d= = 16.25
cos ɸ = 12 = 0.738
16.25
E = 18000 x 0.738
16.252
E = 50.31 lux

## Slide 13
During this session we have:
calculated the angles and side lengths of a right-angled triangle
investigated examples for contextualising the application of trigonometry
solved worked examples of contextualised trigonometry.

## Slide 14
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hertford Regional College has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK